## Slide 1: Stall For Mem Core

## Slide 2: Summary
Most logic is combinational. However, both instruction and data memory are expected to take non-zero clock cycles to return data.
  Upon seeing read/write high, the memory block waits up to N cycles before providing read data or processing a write. The “ready” output is made high for one cycle at this point.
2 additional regs are needed – instruction[31:0] and dmem_data[DATA_WIDTH-1:0]
The processor needs an FSM with the following states -
  ReqInstr
  Wait4Instr
  Wait4ReadData
  Wait4DataWrite

## Slide 3: FSM Flow For All Instructions
ALU/ALUI, LUI, AUIPC, BXX, JAL, JALR –
  ReqInstr  Wait4Instr (after 1 cycle)
  Wait4Instr  ReqInstr (after instr_ready_i is 1)
SB, SH, SW
  ReqInstr  Wait4Instr (after 1 cycle)
  Wait4Instr  Wait4DataWrite (after instr_ready_i is 1)
  Wait4DataWrite  ReqInstr (after dmem_ready is 1)
LB, LH, LW, LBU, LHU
  ReqInstr  Wait4Instr (after 1 cycle)
  Wait4Instr  Wait4ReadData (after instr_ready_i is 1)
  Wait4ReadData  ReqInstr (after dmem_ready is 1)

## Slide 4: Auxiliary Signals + Modification of existing ones
instruction_complete – pulses high during last cycle of Wait4Instr, Wait4DataWrite or Waitmove4ReadData, depending upon instruction type. This should the FSM into the ReqInstr state.
read_instr_o – pulses high in the ReqInstr state.
regfile_wen_r – pulses high during last cycle of Wait4Instr or Wait4ReadData, depending upon instruction type.
dmem_write_o – pulses high during last cycle of Wait4Instr for SB, SH and SW.
dmem_read_o – pulses high during last cycle of Wait4Instr for LB, LH, LW, LBU and LHU.
Other control signals are driven combinationally, with the assumption of 0 delay (or satisfactory path delay).
For instance – when the instruction is loaded (instr_ready_i == 1), the actual dmem_write/read output from dmem_input_and_ctrl_logic will remain high until the memory access is fully processed. The dmem_write/read_o signals on the other hand, would only be asserted during the cycle when instr_ready_i is up.

## Slide 5: Stats + Possible Improvements
For linked_list.c, single_cycle_core takes ~4.78us to execute, where as stall_for_mem_core takes ~30.75us. This (6.43x slowdown) is expected with the slower non-zero latency memory. A few improvements can be made here –
  The instruction and data memory accesses can be pipelined  core : stall4mem_pip_core
  (Assuming it’s feasible) Both instruction and data memory can utilize caches which fetch blocks of words. *perhaps with the assumption that this comes at the cost of greater latency  stall4mem_

## Slide 6: Stall For Mem Pipelined Core

## Slide 7: Notes
In the current implementation, since all sub-blocks (except memory) are combinational, memory access latency is the rate-limiting factor.
Goal – always be performing some instruction fetch, and / or some data memory access. Process whatever can be processed.
Constraints – In order commits to RegFile and Data Memory.
Implementation – Two stage pipeline – (IF+ID+EX) stage and MEM stage. WB is derived combinationally from these two.
  (IFIDEX) should always try to fetch an instruction. Simplification – no instruction buffer. Only fetch another one if the current one is complete, or can move out of this stage.
  Memory stage should always try to process a memory access.

## Slide 8: Dependency Table + Hazards
 | operands needed |  | produces rd? | instruction complete at |  | 
 | rs1 | rs2 |  | IF+ID+EX | mem write | mem read + ready
R | yes | yes | yes | yes | - | -
I (non-load) | yes | no | yes | yes | - | -
I (load) | yes | no | yes | no | - | yes
S | yes | yes | no | no | yes | -
B | yes | yes | no | yes | - | -
U | no | no | yes | yes | - | -
J | no | no | yes | yes | - | -
Structural Hazards :
  only one instruction can access data memory at once.
  only one instruction can write to the RegFile at once.
Data Hazards : any (load) instructions that produce an (rd) that conflicts with (rs1 or rs2) the next instruction
Control Hazards : none (branch and jump instructions complete as soon as they are fetched)

## Slide 9: Instruction Groups
Groups of instructions –
U, J – can be completed as soon as instruction is fetched.
B – can be completed as soon as the instruction is fetched, as long as operands are ready.
R, I (non-load) – can be completed as soon as instruction is fetched, long as operands are ready and a previous regfile write asisn’t in progress.
I (load) – needs to wait for the operand to be ready before it issues a dmem_read ; it can be completed only when the read data is fetched, and a previous regfile write isn’t in progress.
S – needs to wait for the operand to be ready before it issues a dmem_write.
* One complication that arises due to S instructions not waiting for the dmem_ready signal is that subsequent instructions must stall to perform any memory operations.

## Slide 10: Flow for each group of instructions
[1] type instructions can be completed when (instr_ready_i == 1) AND (wait4regfile_write == 0)
[2] type instructions (B) can be completed once (instr_ready_i == 1) AND (operands_ready == 1)
[3] type instructions can be completed once (instr_ready_i == 1) AND (operands_ready == 1) AND (wait4regfile_write == 0)
[4] type instructions –
  issue a dmem_read once (operands_ready == 1) AND (wait4dmem_ready == 1) AND (instr_ready == 1).
  Can be completed once (dmem_ready_i == 1) AND (wait4regfile_write == 0).
[5] type instructions –
  Can issue a dmem_write once (operands_ready == 1) AND (wait4dmem_ready == 1). At this point, the instruction is complete, wait4dmem_ready needs to be set to 1.

## Slide 11: Potential Stalls
[1] followed by [1-5]  no stalls.
[2] followed by [1-5]  no stalls.
[3] followed by [1-5]  no stalls.
[4] followed by –
  [1] : no operand dependency, but stall if same rd.
  [2] : stall if operands are same as rd of [4].
  [3] : stall if operands are same as rd, or if same rd.
  [4, 5] : stall if memory is busy
[5] followed by –
  [1-3]  no stalls
  [4, 5] : stall if memory is busy
Notes: instructions [1-3], do not cause any subsequent instructions to stall by themselves.
[1] should be stalled if it has a preceding [4] that writes to the same rd (in order commit, although technically, the rd value would be overwritten)
[3] should be stalled similarly ; and there’s a RAW dependency for [2, 3] instructions followed by [4] (if the operands match rd)
[4, 5] need to be stalled if memory is busy (i.e. if they’ve been preceded by a [4, 5] instruction that has possibly been fetched really soon)

## Slide 12: New Signals, Stalls, Forwarding
Pipeline Stages –
  IFIDEX stage
  MEM stage
  (combinational) WB logic
Modules within core (except stages) –
  RegFile