## Slide 1: Stall For Mem Core

## Slide 2: Summary
Most logic is combinational. However, both instruction and data memory are expected to take non-zero clock cycles to return data.
  Upon seeing read/write high, the memory block waits up to N cycles before providing read data or processing a write. The “ready” output is made high for one cycle at this point.
2 additional regs are needed – instruction[31:0] and dmem_data[DATA_WIDTH-1:0]
The processor needs an FSM with the following states –
  ReqInstr
  Wait4Instr
  ReqReadData
  Wait4ReadData
  ReqDataWrite
  Wait4DataWrite