## Slide 1: A RISC-V PROCESSOR DESIGN & SIMULATION ENVIRONMENT
Mrinav Saxena

## Slide 2: Background
I’m revising Computer Organization And Design (The Hardware/Software Interface: RISC-V Edition) by Patterson and Hennessy.
Earlier in 2020, when I took up Computer Architecture in college, I implemented a basic RISC-V processor in Verilog. I incorporated several architectural optimizations which I read about in Patterson & Hennessy.
To simulate (and carry out rudimentary verification on) my implementation, I wrote a script to translate RISC-V assembly to machine code, which I then loaded into my testbench during a run. Reviews were manual.
Having worked as a design verification engineer in the industry for 4 years, I wanted to revisit this.

## Slide 3: Intent
In order to correlate my learnings with actual code, I am setting up an environment which would take -
  a C file (or project), and
  a processor-memory testbench
… and simulate a run of this code – testbench pair.
It should support –
  Multiple test sequences (different C files as testcases, or mini-benchmarks)
  Multiple testbenches (to separate different implementations, and compare them on different runs)
It would also be nice to have a verification set-up in order to gauge the functional correctness of an implementation, as well as extract its performance metrics.

## Slide 4: Abstract
This environment is based on one top-level script that (as of now) –
  Compiles a particular C file, and builds the corresponding ELFs and .hex files
  Compiles the HDL design and testbench files
  Runs this simulation
Tools and Languages of choice (I’m running this on Windows PowerShell) –
  GCC (riscv-none-elf-gcc) to compile C code
  Verilator to compile the design and testbench
  C++ for the top level TB wrapper
  SystemVerilog for RTL and TBs
  Python for the top-level script

## Slide 5: File Structure (so far)
riscv_verif0
  code (C files)
    (e.g.) rv32i_coverage.c
  rtl (SystemVerilog files)
    core
      single_cycle
    mem
      mem_zerolat
  sim
    build (contains Verilator outputs)
    images (contains ELFs, disassembly and hex files)
    scripts
    runs
      (e.g.) rv32i_coverage_on_sanity
        log files, disassembly and hex files
        dump.fst (wavedump)
  tb
    (e.g.) sanity

## Slide 6: sim/scripts/run run_sim.py
Primary arguments :
  -code  C file which is compiled for a run
  -tb  path to testbench directory for a run
Flow :
  Create run directory – sim/runs/<c_filename>_on_<tb_dir_name>
  Compile C code (riscv-none-elf-gcc) and build hex files
    ELFs, .bin, .disasm, .s and .hex files generated in sim/images/<c_filename>
  Copy hex files into run directory
  Run verilator command
    Build files generated in sim/build/<c_filename>_on_<tb_dir_name>
  Build verilated make
  Run simulation (sim/build/V<tb_filename>.exe)

## Slide 7: sim/scripts/run run_sim.py
Notes
  (Currently) imem.hex and dmem.hex are generated separately during the C build phase.
  <tb_dir_path>/startup.s was needed to ensure PC jumps to main() after it starts (from 0x00).
  Arguments –CFLAGS and –LDFLAGS in the verilator command are a workaround since it wasn’t able to find zlib.h. (Also, -DWIN32 -D_WIN32 -D__MINGW64__).
  Environment variable VERILATOR_ROOT is being set before running the make command.
  Also, MINGW64 bin path is given priority over Cygwin GCC as the make command confuses the two otherwise.
  sys.stdout.flush() is just to flush the terminal output, otherwise line breaks might not be processed correctly during and after the make step.

## Slide 8: Env Plan
In order to check the functional correctness of an implementation, the plan is to –
  Compare any test run’s resultant memory (res_dmem.hex) with that of the same test on single_cycle_core.
  Compare pc_seq.hex to confirm that fetch order is the same, though this will become problematic if pre-fetch / speculative logic is added.
  Find a way to confirm if commits are in order.
Some infra in the testbench (needs to be common and easily importable) for building a tarmac log.
From a performance perspective, some infra is needed to tally CPI, stalls, etc.

## Slide 9: TBD
Environment
  Add testbench infra / classes that run checks on code
  Add testbench infra / classes that track execution performance
Implementation
  Exceptions, Traps and Interrupts
  Pipelined Multi Cycle Core, hierarchical memory

## Slide 10: References
https://veripool.org/guide/latest/exe_verilator.html
https://cass-kul.github.io/