## Slide 1: Single Cycle Core

## Slide 2: Summary (single_cycle_core.sv)
All logic is combinational; memory is expected to provide data instantaneously. PC is incremented / changed on posedge clk.
Logical blocks (apart from PC, ALU, imm_gen) –
  PC logic
  RegFile inputs, control signals
  ALU inputs, control signals
  Data memory inputs, control signals
  Regfile write logic

## Slide 3: Inter-stage dependencies
PC logic
RegFile inputs, control signals
ALU inputs, control signals
Data memory inputs, control signals
Regfile write logic
PC
IMem Interface
RegFile
DMem Interface
[2]
[3]
Imm
Gen
[4]
[5]
[1]
Notes: A very rough schematic of the sub-blocks interconnected between the processor’s major components (PC, RegFile, Immediate Data Generator, ALU) and the memory interfaces. Line colours just differentiate intersecting signals in the schematic.

## Slide 4: Inter-stage dependencies
PC logic
RegFile inputs, control signals
ALU inputs, control signals
Data memory inputs, control signals
Regfile write logic
*Each of these stages are implicitly dependent upon instruction[31:0]. Other small pieces of logic (such as PC+4) have also not been listed.
PC logic
  Imm Gen (for JAL and Branch instructions)
  ALU Result (for JALR)
RegFile inputs, control signals (except for write ports) - None
ALU inputs, control signals
  RegFile Data
  Imm Gen
Data memory inputs, control signals
  RegFile Data
  ALU Result
RegFile write logic
  ALU Result
  Data Memory output