## Slide 1: Stall For Mem Core

## Slide 2: Summary
Most logic is combinational. However, both instruction and data memory are expected to take non-zero clock cycles to return data.
  Upon seeing read/write high, the memory block waits up to N cycles before providing read data or processing a write. The “ready” output is made high for one cycle at this point.
2 additional regs are needed – instruction[31:0] and dmem_data[DATA_WIDTH-1:0]
The processor needs an FSM with the following states -
  ReqInstr
  Wait4Instr
  Wait4ReadData
  Wait4DataWrite

## Slide 3: FSM Flow For All Instructions
ALU/ALUI, LUI, AUIPC, BXX, JAL, JALR –
  ReqInstr  Wait4Instr (after 1 cycle)
  Wait4Instr  ReqInstr (after instr_ready_i is 1)
SB, SH, SW
  ReqInstr  Wait4Instr (after 1 cycle)
  Wait4Instr  Wait4DataWrite (after instr_ready_i is 1)
  Wait4DataWrite  ReqInstr (after dmem_ready is 1)
LB, LH, LW, LBU, LHU
  ReqInstr  Wait4Instr (after 1 cycle)
  Wait4Instr  Wait4ReadData (after instr_ready_i is 1)
  Wait4ReadData  ReqInstr (after dmem_ready is 1)

## Slide 4: Auxiliary Signals + Modification of existing ones
instruction_complete – pulses high during last cycle of Wait4Instr, Wait4DataWrite or Waitmove4ReadData, depending upon instruction type. This should the FSM into the ReqInstr state.
read_instr_o – pulses high in the ReqInstr state.
regfile_wen_r – pulses high during last cycle of Wait4Instr or Wait4ReadData, depending upon instruction type.
dmem_write_o – pulses high during last cycle of Wait4Instr for SB, SH and SW.
dmem_read_o – pulses high during last cycle of Wait4Instr for LB, LH, LW, LBU and LHU.
Other control signals are driven combinationally, with the assumption of 0 delay (or satisfactory path delay).
For instance – when the instruction is loaded (instr_ready_i == 1), the actual dmem_write/read output from dmem_input_and_ctrl_logic will remain high until the memory access is fully processed. The dmem_write/read_o signals on the other hand, would only be asserted during the cycle when instr_ready_i is up.

## Slide 5: Stats + Possible Improvements
For linked_list.c, single_cycle_core takes ~4.78us to execute, where as stall_for_mem_core takes ~30.75us. This (6.43x slowdown) is expected with the slower non-zero latency memory. A few improvements can be made here –
  The instruction and data memory accesses can be pipelined  core : stall4mem_pip_core
  (Assuming it’s feasible) Both instruction and data memory can utilize caches which fetch blocks of words. *perhaps with the assumption that this comes at the cost of greater latency  …

## Slide 6: Stall For Mem Pipelined Core

## Slide 7: Notes
In the current implementation, since all sub-blocks (except memory) are combinational, memory access latency is the rate-limiting factor.
Goal – always be performing some instruction fetch, and / or some data memory access. Process whatever can be processed.
Constraints – In order commits to RegFile and Data Memory.
Implementation – Two stage pipeline – (IF+ID+EX) stage and MEM stage. WB is derived combinationally from these two.
  (IFIDEX) should always try to fetch an instruction. Simplification – no instruction buffer. Only fetch another one if the current one is complete, or can move out of this stage.
  Memory stage should always try to process a memory access.

## Slide 8: Dependency Table + Hazards
 | operands needed |  | produces rd? | instruction complete at |  | 
 | rs1 | rs2 |  | IF+ID+EX | mem write | mem read + ready
R | yes | yes | yes | yes | - | -
I (non-load) | yes | no | yes | yes | - | -
I (load) | yes | no | yes | no | - | yes
S | yes | yes | no | no | yes | -
B | yes | yes | no | yes | - | -
U | no | no | yes | yes | - | -
J | no | no | yes | yes | - | -
Structural Hazards :
  only one instruction can access I/D memory at once.
  only one instruction can write to the RegFile at once.
Data Hazards : any (load) instructions that produce an (rd) that conflicts with (rs1 or rs2) the next instruction.
Control Hazards : none (branch and jump instructions complete as soon as they are fetched).

## Slide 9: Instruction Groups
Groups of instructions –
U, J – can be completed as soon as instruction is fetched.
B – can be completed as soon as the instruction is fetched, as long as operands are ready.
R, I (non-load) – can be completed as soon as instruction is fetched, long as operands are ready and a previous regfile write asisn’t in progress.
I (load) – needs to wait for the operand to be ready before it issues a dmem_read ; it can be completed only when the read data is fetched, and a previous regfile write isn’t in progress.
S – needs to wait for the operand to be ready before it issues a dmem_write.
* One complication that arises due to S instructions not waiting for the dmem_ready signal is that subsequent instructions must stall to perform any memory operations.

## Slide 10: Flow for each group of instructions
[1] type instructions can be completed when (instr_ready_i == 1) AND (wait4regfile_write == 0)
[2] type instructions (B) can be completed once (instr_ready_i == 1) AND (operands_ready == 1)
[3] type instructions can be completed once (instr_ready_i == 1) AND (operands_ready == 1) AND (wait4regfile_write == 0)
[4] type instructions –
  issue a dmem_read once (operands_ready == 1) AND (wait4dmem_ready == 1) AND (instr_ready == 1).
  Can be completed once (dmem_ready_i == 1) AND (wait4regfile_write == 0).
[5] type instructions –
  Can issue a dmem_write once (operands_ready == 1) AND (wait4dmem_ready == 1). At this point, the instruction is complete, wait4dmem_ready needs to be set to 1.

## Slide 11: Potential Stalls
[1] followed by [1-5]  no stalls.
[2] followed by [1-5]  no stalls.
[3] followed by [1-5]  no stalls.
[4] followed by –
  [1] : no operand dependency, but stall if same rd.
  [2] : stall if operands are same as rd of [4].
  [3] : stall if operands are same as rd, or if same rd.
  [4, 5] : stall if memory is busy
[5] followed by –
  [1-3]  no stalls
  [4, 5] : stall if memory is busy
* 4.1 and 4.2 can be optimized if the same rd is written
* based on the above, the signals operands_ready, wait4regfile_write and wait4dmem_ready only apply to the instruction in the first stage.
Notes: instructions [1-3], do not cause any subsequent instructions to stall by themselves.
[1] should be stalled if it has a preceding [4] that writes to the same rd (in order commit, although technically, the rd value would be overwritten)
[3] should be stalled similarly ; and there’s a RAW dependency for [2, 3] instructions followed by [4] (if the operands match rd)
[4, 5] need to be stalled if memory is busy (i.e. if they’ve been preceded by a [4, 5] instruction that has possibly been fetched really soon)

## Slide 12: Stage Buffers
The dmem stage inputs do not need to be buffered as the ifidex stage is stalled until the memory request has been made.
Some inputs to the writeback logic (only those involved in the writeback data for load instructions) do need to be buffered –
  alu_result_i
  instr_type_i
  opcode_i
  * dmem_rdata_i
Any such instruction’s rd also needs to be buffered.

## Slide 13: Result
linked_list.c completes in 24.84us on stall4mem_pip_core  that’s a 19.21% improvement over the non-pipelined implementation.

## Slide 14: Stall For Mem Pipelined + Split Cache

## Slide 15: Notes
Add an instruction cache and data cache to existing implementation. For the purpose of fair comparison, block size of the caches will be 1.
  This is because it’s complicated to estimate the comparative latency of a memory module that otherwise fetches data / processes a write in $urandom_range(1,N) cycles.
Possible DCache implementations –
  Direct Mapped, Set Associative or Fully Associative
  Write Through + No Write Allocate or Write Back + Write Allocate
Modification needed – FSMs need to operate so they can fetch data/instructions every subsequent cycle.
More benchmark C tests are needed to compare all the implementations so far.